Software Requirements Specification
For
The OpenBowling Project
Version 0.xx
Prepared by Matt Mead
Nov. 11, 2009
Table of Contents

Revision History
Name	Date	Reason For Changes	Version
Matt Mead	MM/DD/YYYY	Original Release	0.xx

# Introduction
## Purpose
This document defines the requirements for The Open Source Bowling Project. This is a bowling scorer project for small to medium size bowling centers. This product will read the standing bowling pins after each ball, display the scores to the bowlers and send the bowling data to the front desk for billing or printing, etc.

This is an Open Source project and will be distributed under a common Open Source public license.
## Document Conventions
The requirements listed in this document will use the term “shall”. The terms “will” or “should” or “must” shall not be used in the requirement text. The requirements will use a unique sequence numbering system for each requirement identifier. The requirement identifiers shall be used in other documents and software to reference, verify and test the requirement functionality.

Each requirement will have the following attributes:
- Requirement Identifier (SRS-xxxx)
- Requirement Text (clear, specific and can stand alone)
- Rationale (why the requirement is necessary)
- Priority (1 – 5: 1 = really important (must have); 5 = nice to have)
## Intended Audience and Reading Suggestions
This document is intended mainly for developers and potentially for customers / users, such as bowling center proprietors, mechanics, etc. All requirements must be linked to the design document(s). The requirement sections below may be difficult to read, but are very necessary to capture “what” the system is suppose to do. The design document(s) will define “how” the system will work.
## Project Scope
This is a bowling scorer project for small to medium size bowling centers that may not have automated scoring. The project will consist of 4 different hardware components:
- Pinsetter Interface / Scorer
- Upper Display
- Lower Display / User Input
- Front Desk

The Pinsetter Interface / Scorer device (Scorer) will be located on the capping between 2 pinsetters of a lane pair. It will be able to verify when a ball was thrown and which pins remain standing (after the ball was thrown but before the pins are raked).

The Upper Display device (Upper) will be located over the lane and above the approach (hanging from the ceiling). This allows the bowlers can see the current scorers or other items that may be displayed. The display will probably be a flat screen LCD TV or equivalent device.

The Lower Display / User Input device (Lower) will be located behind the ball return and possibly at a table were the bowlers can sit and enter their data (bowler name, etc). It will probably have a touch screen similar to a Point-Of-Sale device or some equivalent mechanism to enter data.

The Front Desk device (Front) will be used to turn the scorers, uppers and lowers on / off. It will collect the bowling game data when requested.

The Uppers and Lowers will probably have an overlapping software code base for items like graphics, since they both have displays.

For more information, refer to The Open Source Bowling Project Scope document.
## References
<List any other documents or Web addresses to which this SRS refers. These may include user interface style guides, contracts, standards, system requirements specifications, use case documents, or a vision and scope document. Provide enough information so that the reader could access a copy of each reference, including title, author, version number, date, and source or location.>
# Overall Description
## Product Perspective
This is a new product. To our knowledge no other company has developed or release a bowling scorer like this concept. This product is not intended to compete with commercial products from large companies like QubicaAMF, Brunswick, Steltronic, etc. This product should be designed to be as hardware (motherboards, touch screens, camera, etc) independent as possible, so the hardware can be updated or replaced with a different brand or model and still function properly. The intent is to allow small bowling centers to purchase the hardware as needed and when their budget permits to eventually (over time) update a lane or lane pair until all of the lanes have automatic scoring.
## Product Features
The major features include the following:
- Register bowlers by name
- Register when a ball is thrown
- Sense the standing pins after each ball thrown
- Scorer the game
- Display the scores for each bowler
See section 3.System Features for details.
## User Classes and Characteristics
Most of the users will be unskilled in software or technical aspects of this project. This should be kept in mind during the development process.
Bowler: The largest user. Enter names and other user info if needed. Make score corrections when necessary. Select available options for the bowling session. Future options may include IM or texting other bowlings on different lanes or over the internet (if the bowling center has internet access). Other options will be added after the initial development is competed.
Front Desk Personnel: Turn the scorers on/off. Collect the games / balls thrown for payment. Upper / TV controlling (volume, channel, etc). Reset the scorer software or reboot the unit in case of a problem (includes the pinsetter/scorer, Uppers and Lowers). Calibrate the pin spotter cameras and software, if needed.
Mechanic (occasional user): general maintenance, troubleshooting and repair. Utilities need to be in place to support troubleshooting. Calibrate the pin spotter cameras and software, when needed.
Installers (one time user): Install power outlets if needed (electrician). Mount the hardware devices according to the installation instructions. Load the software on the devices. Install and connect all Ethernet cables and switches. Calibrate the pin spotter cameras and software. Test all of the installed devices (run BIT software and do connectivity testing).
Software Updater (from internet or front desk): Update the core software when new releases are available.
## Operating Environment
General: The system will be indoors. There will be vibration from several mechanical devices (pinsetters, ball returns, bowlers hitting the devices, etc), so the equipment will need to withstand the hazards. Because of this, there should be no moving or spinning parts (hard drives, CDs or DVDs, etc). Many bowling centers are rather smokey.
Computer Devices: The computer platform will be mini-ITX or micro-ATX form factor (or others in the future). It would be optimal to be fanless. The software should support different CPU manufacturers especially the main manufactures for the form factors chosen (Intel, AMD, VIA). The operating system will need to sample the hardware and load the proper drivers. This will be a Linux system with a live CD (Knoppix) type of startup sequence. Some bowling centers don't have good air conditioning, so the computers need to run cool.
## Design and Implementation Constraints
- The software will be developed in C / C++ since almost all microprocessors have compilers for those languages.
- 3D graphics are planned for the Uppers and Lowers, so a decent graphics card / chip set will be needed. OpenGL will be used for the 3D graphics.
- The software should be designed for 32 or 64 bit processors and little or big endian processors
- The system should be reliable and small, so Linux will be used as the operating system.
- The system will be similar to a live CD (Knoppix) type of startup sequence to sample the hardware and load the correct drivers.
- Memory: 500MB minimum to support the OS and applications.
- There will be an Interface Control Document (ICD) to capture the communication protocol.
- Qt will be used for the graphics. This will give a standard look to all of the screens regardless of the target or host development platforms.
## User Documentation
There will be an installers guide located in the same location as this document.
A wiki will be created at Google.
A user forum will be created at the project web site.
## Assumptions and Dependencies
Known open source dependencies: Grub, Linux kernel, Morphix / Knoppix (or other Linux distro), OpenGL, XML parser (expat or libxml2), Qt,
It is assumed that pinsetter control is outside this project and this project will not affect the pinsetter operation. League management is also outside this project along with center management and any type of Point-Of-Sale (POS) system.
# System Features
This section holds the system feature requirements. The priority is from 1 to 5 (1 = highest, 5 = lowest).
## Pinsetter
The pinsetter feature recognizes when a ball is thrown and which pins remain standing.
SRS-0001	Priority: 1
Text: The pinsetter device shall determine when a ball is thrown.
Rationale: The ball or rake will determine when the pins should be analyzed. This is a critical requirement.

SRS-0002	Priority: 1
Text: The pinsetter device shall determine which pins are standing after a ball is thrown.
Rationale: The camera will need to take a picture and process it to determine if a pin is standing or fallen. This is a critical requirement.

SRS-0003	Priority: 4
Text: The pinsetter device shall be mounted by the pinsetter within a 5 feet.
Rationale: The device needs to be close to the pinsetters to lower confusion with the mechanic or anyone troubleshooting the system.

SRS-0004	Priority: 1
Text: The pinsetter device shall communicate with other devices using the protocol defined in the ICD.
Rationale: The ICD will be contain the interface standards for all of the devices connected to the system.

SRS-0005	Priority: 1
Text:
Rationale:

SRS-0006	Priority: 1
Text:
Rationale:

SRS-0007	Priority: 1
Text:
Rationale:

SRS-0008	Priority: 1
Text:
Rationale:

## Scorer
## Graphics
# External Interface Requirements
## User Interfaces
Screens.
<Describe the logical characteristics of each interface between the software product and the users. This may include sample screen images, any GUI standards or product family style guides that are to be followed, screen layout constraints, standard buttons and functions (e.g., help) that will appear on every screen, keyboard shortcuts, error message display standards, and so on. Define the software components for which a user interface is needed. Details of the user interface design should be documented in a separate user interface specification.>
## Hardware Interfaces
Serial port (TV and pinsetters), USB 2.0 (2 ports min - TV, web cams), Graphics (RBG/VGA, HDMI), Ethernet, pointing devices (touchscreen, mouse)
<Describe the logical and physical characteristics of each interface between the software product and the hardware components of the system. This may include the supported device types, the nature of the data and control interactions between the software and the hardware, and communication protocols to be used.>
## Software Interfaces
<Describe the connections between this product and other specific software components (name and version), including databases, operating systems, tools, libraries, and integrated commercial components. Identify the data items or messages coming into the system and going out and describe the purpose of each. Describe the services needed and the nature of communications. Refer to documents that describe detailed application programming interface protocols. Identify data that will be shared across software components. If the data sharing mechanism must be implemented in a specific way (for example, use of a global data area in a multitasking operating system), specify this as an implementation constraint.>
## Communications Interfaces (ICD)
<Describe the requirements associated with any communications functions required by this product, including e-mail, web browser, network server communications protocols, electronic forms, and so on. Define any pertinent message formatting. Identify any communication standards that will be used, such as FTP or HTTP. Specify any communication security or encryption issues, data transfer rates, and synchronization mechanisms.>
# Other Nonfunctional Requirements
## Performance Requirements
<If there are performance requirements for the product under various circumstances, state them here and explain their rationale, to help the developers understand the intent and make suitable design choices. Specify the timing relationships for real time systems. Make such requirements as specific as possible. You may need to state performance requirements for individual functional requirements or features.>
## Safety Requirements
<Specify those requirements that are concerned with possible loss, damage, or harm that could result from the use of the product. Define any safeguards or actions that must be taken, as well as actions that must be prevented. Refer to any external policies or regulations that state safety issues that affect the product’s design or use. Define any safety certifications that must be satisfied.>
## Security Requirements
<Specify any requirements regarding security or privacy issues surrounding use of the product or protection of the data used or created by the product. Define any user identity authentication requirements. Refer to any external policies or regulations containing security issues that affect the product. Define any security or privacy certifications that must be satisfied.>
## Software Quality Attributes
<Specify any additional quality characteristics for the product that will be important to either the customers or the developers. Some to consider are: adaptability, availability, correctness, flexibility, interoperability, maintainability, portability, reliability, reusability, robustness, testability, and usability. Write these to be specific, quantitative, and verifiable when possible. At the least, clarify the relative preferences for various attributes, such as ease of use over ease of learning.>
# Other Requirements
<Define any other requirements not covered elsewhere in the SRS. This might include database requirements, internationalization requirements, legal requirements, reuse objectives for the project, and so on. Add any new sections that are pertinent to the project.>
Appendix A: Glossary
<Define all the terms necessary to properly interpret the SRS, including acronyms and abbreviations. You may wish to build a separate glossary that spans multiple projects or the entire organization, and just include terms specific to a single project in each SRS.>
Appendix B: Analysis Models
<Optionally, include any pertinent analysis models, such as data flow diagrams, class diagrams, state-transition diagrams, or entity-relationship diagrams.>
Appendix C: Issues List
< This is a dynamic list of the open requirements issues that remain to be resolved, including TBDs, pending decisions, information that is needed, conflicts awaiting resolution, and the like.>

Matt's Items to remember:
- Switch or proximity sensor for pinsetter ball thrown
- Send ball thrown status over network once a second or on transitions
- Standing pin sensing
- Heart beat messages
- XML for network interfaces. Supports UTF-8 & UTF-16 for Unicode encoding. Use the XML declaration to define the encoding. Exception is data packets (web cam picture, etc) TFTP or FTP?
- Use expat or libxml2 or equivalent for XML encoding
- Have a utility that logs the current version of all relevant software on the box
- COTS hardware when available
- TV interfaces – turn on/off, switch channel (serial interface?)
- Configuration files (TV type, web cams, lane number, host name, etc)
- Log files (flash memory limitations)
- Create an ICD
- 10-pin scoring with 3 balls per frame supported
- Startup withing 3 minutes (2 minutes preferred)
- Startup sequence samples the hardware to load the proper drivers
- Multi-threaded to keep performance high
- Interrupt based – not polling
- No moving or spinning parts – all solid state, because of high vibration and shock
- Intercom (VOIP) system – low priority
- Error reporting (XML parsing errors, etc)
- Screen resolution 1024 x 768 minimum
- Screens for scoring should be scalable to many sizes. May be embedded in a frame of a window to sports scores can scroll across the bottom and other information can be displayed in other frames.
- Software updates (TFTP or FTP). Have to update the read-only partition, etc?
- Support up to 40 lanes for small to medium centers (normal 10 or less).
- Maintenance: the cameras will need to cleaned regularly especially in smokey environments.

Prototype items:
- Pinsetter switch signals. Use RS232 (DB9) or parallel port?
- Pinsetter web cam with Linux
- Analyzing picture of pins and sending data to other computers – embed picture file in XML?or FTP / TFTP instead (Qt has an FTP class)? Same issue with software updates and image / exciter / advertisement updates.

Utilities:
- Configuration file to sum up all relevant software versions
- Pinsetter ball indicator
- Software updater / installer
- Testing software. BIT – Built In Test software to help troubleshoot issues.
- Assign IP addresses and/or host names for the devices (before first use)