# Prototypes:

## Item 1 – Mini-ITX board running LiveCD Linux with SD-to-IDE (or SATA)
Reason why: The computer boards need to be small, so mini-ITX was chosen. The LiveCD type of install will sample the hardware during each startup. The SD-to-IDE or SD-to-SATA boards will replace the hard drive and be more reliable. Need to verify that all of this works together.
Assigned To: Matt
Prototype Results:

## Item 2 – Pinsetter web cam with Linux
Reason why: Web cams are not supported well in Linux. Need to test the cheap ones made in China. Use the drivers from the French open source developer (http://mxhaard.free.fr/spca5xx.html).
Assigned To: Matt
Prototype Results:

## Item 3 – Qt screen development with OpenGL and “stretch” screens for different resolutions
Reason why: The Qt screens will need to be scalable or stretchable to fit different resolutions. Also need to test the OpenGL capabilities of Qt.
Assigned To:
Prototype Results:

## Item 4 – One computer to drive both upper (or lower) screens with OpenGL (dualhead GPU – not using Xephyr)
Reason why: Using one computer to drive both screens will save money in hardware. Need to verify OpenGL with graphics rendering from the GPU for both screens (not the CPU). May need a nVidia chipset to perform this on a dualhead GPU. Two X servers – one for each screen device? 3D / OpenGL may not be possible for both screens in multiseat mode yet.
(MDM – multiseat display manager, x servers – multiple instances, X RandR)
Assigned To:
Prototype Results:

## Item 5 – One computer to drive both lower screens and input devices (udev / evdev)
Reason why: Using one computer to drive both screens and input devices will save money in hardware. Need to test the multiseat functionality with different input devices without stealing the pointer (mouse) selection from each screen. Two X servers – one for each screen / input device?
Assigned To:
Prototype Results:

## Item 6 – OS updates to the read-only partition (while remaining secure)
Reason why: There needs to be an easy way to update the software from the Front Desk or other computer on the network. Updating the application software should be easy, but the read-only OS partition may be difficult.
Assigned To:
Prototype Results:

## Item 7 – Switch to pinsetter rake arm for ball thrown
Reason why: May need a switch hooked to the RS-232 or parallel port to recognize when a ball was thrown or the reset button was pressed.
Assigned To:
Prototype Results:

## Item 8 – Stream web cam data to other computer
Reason why: This may be needed for troubleshooting or setting up the web cam devices.
Assigned To:
Prototype Results: